## Slide 1: High-speed Hardware random number generator
Using Geiger mode photo detector
Presented by: Dr. Dmitriy Beznosko, Physics Dept., SST, NU

## Slide 2: Motivation
Random numbers are used in simulations (!), encryption, security, calling card number generation, lotteries etc…
From HEP - can use Geiger mode photodetector (MPPC or similar) for simple hardware random number generator
Advantages: low cost, high speed (up to 10Mbits/), simplicity and robustness, small size (USB flash memory or similar)
Technical difficulties: stability, achieving equal distribution
Suitable for UG students’ involvement as introduction into HEP instrumentation for future research work

## Slide 3: Example: Short intro to secure computing
Good random numbers are fundamental to ~all secure computer systems.
Simple example of an attack:
  log into a web site - assigned a unique ID for that session
  Needs to be unique to you and not guessable by someone else.
  If someone else can guess it, they can impersonate you. Same is true for a private key, phone card or coupon #, etc…
Although pseudo-random number generators (PRNG) can generate a sequence of apparently random numbers, they have weaknesses (e.g. they all need a starting seed).
Suppose PRNG used is seeded with the current time, in ms.
  Attacker assumes that your machine time, say, within 10 seconds.
  Attacker knows which PRNG is used or has same code/library
  Then seed for your PRNG is known within ~ 10 seconds range; N = 10 000 000 possible seeds. A modern PC will take no time to generate and try these keys.
        http://security.stackexchange.com/questions/42327/how-does-a-weakness-in-a-random-number-generator-lead-to-a-compromise-of-the-ent
        http://blog.cloudflare.com/why-randomness-matters

## Slide 4: PRNGs and HRNGs
Fast PRNG – weak key. Slow PRNG – few keys, still limited in strength. Result typically is repeatable if given same seed.
Hardware random number generator (HRND) works by providing a source of truly random numbers that don't come from a mathematical process.
Source of randomness can be from radioactive decay (slow), the chaotic motion of fluids (very slow), atmospheric noise (slow), quantum-based, or from other unpredictable systems that can not be guessed by an attacker even if he has an access to a similar or even exactly same device.
Need FAST and SECURE operations

## Slide 5: Other uses of affordable HRNG
banks, various communications and cell phone companies, lotteries
government planning offices in their simulations of the economy growth
scientific Monte-Carlo simulations
      Instead of TRandom1,2,3 
(end-user?) data cryptography
computer games
in classrooms
any other place where large number of true random numbers is required.
EAS animation, parent – proton at 1016 eV using CORSIKA1
1CORSIKA: a Monte Carlo code to simulate extensive air showers., by Heck, D.; Knapp, J.; Capdevielle, J.~N.; Schatz, G.; Thouw, T..~ Forschungszentrum Karlsruhe GmbH, Karlsruhe (Germany)., Feb 1998, V + 90 p., TIB Hannover, D-30167 Hannover (Germany

## Slide 6: Operational Principle
Geiger mode sensor operations are widely known in HEP community
Amount of photons that falls onto the photodiode follows the Poisson distribution - random
If absorbed, produced an eclectic pulse that is detected as digital1 signal (above preset threshold)
QE of photodiode is ~constant (weak dependence on bias and T) and is on the order of ~20-30%
Dark noise within gate – random, rare
Late after-pulse is also random, for gate ~100ns falls with signal, no effect
10Mbits for 100ns gate, can go higher
https://indico.cern.ch/event/41044/session/48/contribution/7/material/slides/0.pdf
K.Abe at. al. (T2K Collaboration), "The T2K Experiment", Nucl. Instrum. Meth. A659 (2011) 106–135 Jun 06, 2011 doi: 10.1016/j.nima.2011.06.067
  1A. Dyshkant, D. Beznosko, G. Blazey, D. Chakraborty, K. Francis, D. Kubik et al., "Small scintillating cells as the active elements in a digital hadron calorimeter for the e+e- linear collider detector" 2004 J. Phys. G: Nucl. Part. Phys. 30 N1-N16

## Slide 7: Experimental Setup
400pixel 1mm2 Hamamatsu MPPC was used
  Pulse Width ~20ns – max. up to 50MHz in theory
  Bias 70.2 ±0.1V slowly changing over time, short time stability better then 0.01V
set a threshold (at ~ -5mV) - separates the pedestal from the signal
  the values below converted into the bit of value 1, and above it to 0
The resultant is the integral probability of signal being detected or not
But its not 50% of 1 and 50% of 0.
  even if tune to have it so, parameters (bias, T, etc…) drift in time
  Can use randomness extractor algorithm (e.g. AMLS1) and local stability (order of a second or less if needed)
  1Peres, Yuval. Iterating von Neumann's Procedure for Extracting Random Bits. The Annals of Statistics, 1992, pp 590-597

## Slide 8: von Neumann's Procedure in AMLS
  P(1)=p, P(0)=1-p
  P(11)=p2, P(00)=(1-p)2, P(10)=p(1-p),P(01)=(1-p)p
  P(10)=P(01) QED
Start with 1 and 0 sequence that is uneven
Fold in half, 00 and 11are skipped
From 01, 10 use first only, discard used, get equal seq.
Can go further and fold resulting in half again
Comes from un-biasing the unfair coin – the transitions between 2 binary states are always ‘fair’
Example:
  101111101010111010111011010111011011111010101001011111: fold
  101111101010111010111011010 111011011111010101001011111
  Take one of the lines with used removed (1st here) and fold again 11111101 11011011

## Slide 9: Output Tests1
For each test, a theoretical result is \known for a sample of ‘perfect’ random data, thus allowing a comparison
Show only most illustrative tests.
Graphical.
  The bits are read by 8 as a single unsigned integer
  Resultant value (0-255) is plotted as a pixel brightness
  No patterns visible
  ‘Birthday’ test also shows good quality, lengthy result and description in 1
1D. Beznosko, T. Beremkulov, A. Duspayev, A. Iakovlev, A. Tailakov, M. Yessenov. "A Physical Principle for Fast and Miniature Random Number Hardware Generator Using MPPC Photo Detector." JOURNAL OF ADVANCES IN PHYSICS [Online], 7.3 (2015): 1970-1975. Web. 19 Jun. 2015
Preprint: D. Beznosko, T. Beremkulov, A. Duspayev, A. Iakovlev, A. Tailakov, M. Yessenov "Random Number Hardware Generator Using Geiger-Mode Avalanche Photo Detector", January 2015, arXiv:1501.05521
Same graphical representation of .pdf file in [1], patterns visible

## Slide 10: Output Tests cont’d
read the data as 16bit signed integers and plot them as a histogram
ENT1 test (sample size dependence. Ideal values for infinite set only)
  ‘ideal’ values: Entropy=8, mean=127.5, chi-test between10% and 90%, correl.=0
Test Name | Result
Entropy | 7.999888 bits per byte
Chi-square Test | 252.64 for 1633342 samples, randomly exceed this value 53% of times
Arithmetic Mean | 127.4651
Monte Carlo Value For Pi | 3.140154916
Serial Correlation Coeffcient | 0.000019
1Walker, John. A Pseudorandom Number Sequence Test Program. http://www.fourmilab.ch/random/

## Slide 11: Prototype design in progress
Work in progress
  Physics part completed
  Needs implementation
  Based on USB microcontroller (Arduino-like, 20MHz)
  Design parts in progress:
    LED driver
    Amplifier + discriminator
    Power up-converter 5-70V
    Compact assembly
  Software
    AMLS implementation
    Streaming of linear distributed numbers (possibly Gaussian as well)
    Output to file of differently distributed random numbers
    User-friendly interface

## Slide 12: Commercialization possibility: Innovative Hi-Speed USB3 Quantum True-Random Number Generator
PC-side software allows to save numbers as file or to feed into another program (via port emulation or network)
  Allows to model linearly distributed random numbers, normal distribution and other common ones.
Internal controller keeps the calibration and ensures quality
Fast operations – ~10 Mbits/sec per sensor
Reliability and Continuous operations
USB (2&3) connectivity
SATA, PCI-E possible
Expected cost ~<$200

## Slide 13: Competitors
Quantis-USB-4M module
        http://www.idquantique.com/random-number-generators/ordering/online-shop.html
  Optical mirror reflection (half-transparent)
  4Mbit/sec (vs. minimal of 10 proposed)
  High cost – €990
ComScire
        http://comscire.com/cart/index.php?main_page=product_info&cPath=0&products_id=4
  Shot noise in transistor – poor source, unstable
  4Mbit/sec (vs. minimal of 10 proposed)
  High cost - $895
ubld.it
        http://ubld.it/products/truerng-hardware-random-number-generator/
  Uses effect in a semiconductor junction - poor source, unstable
  Slow - 350 kilobits/second
  Low cost - $50

## Slide 14: Competitors
Random.org
  Uses atmospheric noise – can be duplicated / compromised if schematic/location is known
  This is slow and large equipment – can not fit inside a computer, transmitted over internet (not secure), bits/sec only
LETech
        http://www.letech.jpn.com/rng/products_e.html
  Uses thermal noise – poor source of randomness, unstable
  Need special processing to improve quality
        Takeshi SAITO, Koichi ISHII, Isao TATSUNO, Susumu SUKAGAWA, Tomotake YANAGITA, “Randomness and Genuine Random Number Generator With Self-testing Functions”, Joint International Conference on Supercomputing in Nuclear Applications and Monte Carlo 2010 (SNA + MC2010)
Pico Quant
        http://www.picoquant.com/products/category/quantum-random-number-generator/pqrng-150-quantum-random-number-generator
  quantum randomness of photon arrival times – good randomness but hard in implementation, unstable
  150 Mbits/s
  Prohibitively high cost €12500

## Slide 15: CONCLUSION
Seeds, keys, phone cards, science simulations etc. require high-quality random numbers
Software generators are weak/slow
Hardware generators are slow/expensive (existing)
Proposed HRNG is affordable, reliable and miniature solution accessible for scientific, large corporate, small office, educational and personal usage.
our focus from early on is on the global consumers

## Slide 16: Existing patents
A. Stefanov et al., at URL: http://xxx.lanl.gov/abs/quant-ph/9907006
US 7197523 B2 -USA
CN 100505540 C -China
Above are generic patents for the actual underlighing idea. The implementation proposed is different and patentable as such.
Related patents: US 20110127415 A1, EP 2592547 A1
Related ideas: US 6393448 B1, WO 2009064167 A2

## Slide 17: Безопасность данных -краткое введение
Качественный генератор случайных чисел (ГСЧ) – основа для всех систем безопасности данных
  Примеры простых атак: подделка сессионного ID, private key, номера телефонной карточки, купона…
В последовательностях, полученных от псевдо-случайного ГСЧ (ПГСЧ), всегда есть уязвимости – как минимум, требуется начальное значение (seed)
Как правило, за seed берется системное время в микросекундах.
  При атаке на сервер, если предположить что время на нем и компьютере хакера в пределах 10 секунд, то нужно проверить лишь 10млн seeds что очень быстро на современном ПК.

## Slide 18: ПГСЧ и АГСЧ
Быстрые ПГСЧ – слабый ключ, хороший ПГСЧ – медленный и мало ключей, ограниченные методом
Аппаратный генератор случайных чисел (АГСЧ) – работает путем предоставления аппаратного (не математического) источника «случайности».
  Это радиоактивный распад (медленно), хаотическое движение жидкости (очень медленно), атмосферные шумы (медленно), и другие непредсказуемые системы которые не могут быть разгаданы хакером даже если он получит доступ к нему.
  Последнее исключает псевдо-АГСЧ как /dev/random(4) в ядре Linux которое использует «хаос» в работе ПК
АГСЧ должен быть БЫСТРЫМ и БЕЗОПАСНЫМ

## Slide 19: Инновационный Высокоскоростной USB3 Квантовый Генератор Случайных Чисел
Предлагаемый АГСЧ использует совершенно непредсказуемую квантово-механическую природу поглощения света фотодетектором. Единичные фотоны при поглощении дают сигнал ‘1’, иначе – ‘0’
Высока скорость – от 10s до 100s Mbits/sec
Надежность и Непрерывность работы
USB (2&3) совместимость
SATA, PCI-E возможность
Также 5.25” модуль
Цена <$200

## Slide 20: Принцип Работы
Свет от светодиода попадает на поверхность фотодетектора
В случае поглощения полученный сигнал фиксируется
Внутренний процессор поддерживается калибровку устройства и качество работы
Программа на ПК позволяет сохранить данные как файл или предоставить их другой программе (через эмуляцию порта или соединение через сеть («localhost»))
Прибор предоставляет линейно распределенные случайные числа, распределенные нормально и по другим распространённым распределениям. Пользовательские функции также могут быть указаны.

## Slide 21: CONCLUSION
Seeds, ключи шифровки, телефонные карточки, научные симуляции и т.д. – все требует высококачественного источника случайных чисел
Программные генераторы медленны/слабы
Аппаратные генераторы медленны/дорогие (существующие))
Предложенное АГСЧ решение является недорогим, доступным и надежным для корпоративного, офисного, образовательного и персонального применения.